## Slide 1: CASTING: Pattern & Allowances
Lecture 2

## Slide 2: Casting
It is the process of producing metallic parts by pouring a molten metal in to the mould and allowing the metal to solidify.

## Slide 3: Casting Process
Mould is prepared
Metal is Heated above Melting Point Temp
Liquid Metal is Poured into Mold
Metal Solidifies into Shape of Mold
Casted Part is Removed from Mold
Post Casting Operations
  Cutting
  Clean Up
  Machining

## Slide 6: Pattern
A pattern is a replica of a casting to be made.
Using pattern, impressions (mould cavity) can be formed in the damp sand to make a mould.

## Slide 7
Wood: easy to work & readily available, can be cut in to required shapes and used when small number of castings
Metal: do not change their shape when subjected to moist condition, used when small number of castings
Plastics: do not absorb moisture, smooth, can be withdrawn from the mold easily, without damaging the mold
Plaster: High compressive strength
Pattern materials

## Slide 8
Green sand mold
with pattern
SECOND OPERATION
Drag
Pattern
Molding board
FIRST OPERATION
Drag
Molding board
Drag
Pattern
Molding board
FIRST OPERATION
Drag
Molding board
Riser pin
Sprue pin
Cope
Parting
line
COMPLETE MOLD
Pouring basin
Weight
Riser
Lifter
Vents
Parting
line
Core
Runner
Gate

## Slide 9
Casting Defect

## Slide 10
Types of patterns
1. Single piece pattern 2. Match plate pattern
3. Gated pattern 4. Split pattern
5. Cope & Drag pattern 6. Loose-piece pattern
7. Skeleton pattern

## Slide 11
Types of patterns

## Slide 12
Match Plate Pattern

## Slide 13
Types of patterns

## Slide 14
Made from one piece & does not contain loose pieces
Inexpensive & are of simplest type
Single piece pattern
Split pattern
Most widely used pattern for intricate castings
Here the pattern is split into 2 parts so that one part is in
the cope & other is in the drag
Two halves of the pattern is aligned properly by using
dowel pins
Types of patterns

## Slide 15
Similar to split patterns
The cope & drag halves of the pattern along with the gating
and riser systems prepared separately
But they are attached separately to the metal or wooden
plate along with alignment pins
Cope and Drag pattern
Match plate pattern
An extension of cope and drag pattern
Here the cope & drag patterns along with the gating &
risering are mounted on a single matching or metal plate
on either side

## Slide 16
Used when contour of the part is such that withdrawing the pattern from the mold is not possible
Obstructing part is held as a loose piece
Loose piece pattern
Skeleton pattern
Made of strips of wood for preparing final pattern
by pouring the sand around the pattern and packing it

## Slide 17
Usually made of metal which increases their strength and reduces tendency to warp
Section connecting different patterns serve as runner and gates
A gated pattern can manufacture many castings at one time
Used in mass production systems
Gated pattern

## Slide 18
Molten Metal Cooling Curve

## Slide 19
Pattern Allowances
Shrinkage allowance
Draft or Taper allowance
3. Machining or Finishing allowance
4. Camber or distortion allowance
5. Shake or Rapping allowance

## Slide 20
Shrinkage allowance
Most of the metals used in casting contract during cooling from pouring temperature to room temperature
Provided to compensate for solid contraction by providing adequate allowances in the pattern
Amount of contraction varies with different metals
Pattern Allowances

## Slide 21
Shrinkage allowance
Pattern Allowances

## Slide 22
2. Machining Allowance
Given on the surface of the pattern by increasing the metal
thickness there to compensate for loss of metal due to
machining on these surfaces
Depends mainly upon method of machining to be employed
Given in addition to the shrinkage allowance
Pattern Allowances

## Slide 23
Pattern Allowances
Machining Allowance

## Slide 24
Given slight taper on the vertical surfaces of the pattern
parallel to the direction of withdrawal from the mould
Provided on both internal & external surfaces
For easy withdrawal of pattern from the mould
3. Draft or Taper allowance
Pattern Allowances

## Slide 25
Draft or Taper allowance
Pattern Allowances

## Slide 26
Negative allowance to be provided in the pattern
When pattern is withdrawn from the mould by striking over
it from side to side, size of the cavity increases
To compensate this rapping allowance is provided
4. Rapping allowance
Pattern Allowances

## Slide 27
Rapping allowance
Pattern Allowances

## Slide 28
Castings having irregular shape, will not have uniform
contraction during their cooling
Results in distortion of the castings
Remedy:
An opposite distortion is provided in the pattern
5. Distortion allowance
Pattern Allowances

## Slide 29
Distortion allowance
Pattern Allowances

## Slide 30
11